## Slide 1: Automated Guided Vehicle AGVs
Matric: 1523889

## Slide 2: Introduction and history
What is an AGV ?
It is an Automated Guided Vehicle system (AGVs), is a material handling system that uses independently operated ,self-propelled vehicles guided along defined pathways on the floor. We cloud say is a portable robot that follows along marked long lines.Sometimes called self-guided vehicles.
Arthur “Mac” Barrett built the first automatic guided vehicle in 1953 by modifying a towing tractor so that it followed an overhead wire. His company, Barrett Electronics Corporation, debuted his driverless vehicle in 1954, calling it the Guide-o-Matic. Essentially, the Guide-o-Matic was a tow truck that automatically followed a wire embedded in the floor.

## Slide 3: Types of AGVs:
There are several types of automated guided vehicles and it operate without direct human intervention or guidance.
Types of AGVs
Automated Guided Carts
An automatic guided cart (AGC) is the most basic type of AGV with minimal features.
Forklift AGVs It is automated guided vehicles, which are another commonly used type of AGV. They are designed to perform the same function but without the need for a human operator.
Unit Load Handlers
Unit load handlers carry discrete loads such as individual objects, or a single unit such as a pallet or tote that contains multiple items.
Towing AGVs
Towing vehicles, or tugger automatic guided vehicles, pull one or more non-powered, load-carrying vehicles behind them in a train-like formation.
Autonomous Mobile Robots
Autonomous mobile robots (AMRs) are typically more technologically advanced than other types of AGVs. While many AGVs use fixed navigation systems,
Heavy Burden Carriers
For the heaviest loads, heavy burden carriers are a type of AGV used in applications such as large assembly, casting, coil, and plate transport.

## Slide 4: Applications for AGVs
Automated guided vehicle systems are used for tasks that would typically be handled by :
Forklifts.
Conveyor systems.
Manual carts.
Moving large volumes of material in a repetitive manner.
They’re often used for transporting raw materials such as metal, plastic, rubber or paper.For example, AGVs can transport raw materials from receiving to the warehouse or deliver materials directly to production lines.

## Slide 5: How AGVs work
AGVs are self-propelled vehicles with movement guided by software and sensors. Most AGVs move along defined pathways, but as mentioned, AMRs typically have more advanced technology with dynamic navigation capabilities.

## Slide 6: Design and Customization
When designing your custom AGV system, AGV manufacturers consider all of your application specifications, including: the type of loads to be moved, the sizes and shapes of loads to be moved, the motions required (lifting, loading, assembling, towing, etc.), the size of the facility, the layout of the facility and client budget.
Using these considerations, they pick out system details like: AGV type, guiding mechanism type and AGV programming. For example, during manufacturing, or even later on, manufacturers may program an AGV to perform maneuvers like spinning, moving laterally, raising and lowering and so on.

## Slide 7: Safety and Compliance Standards
AGVs are beholden to a variety of different safety and compliance standards, primarily those put out by ANSI (American National Standards Institute). ANSI puts out a number of different standards that offer information like: guidelines for performance/durability/safety evaluations, recommendations for usage, information on regulatory requirements and the like. Examples of applicable standards include: ANSI ECMA 15-2010 (specs for cable-less controls of electric overhead traveling), ANSI ICWM-2012 (performance standards for castors and wheels), ANSI MH1-2016 (terminology, nomenclature and dimension/size recommendations related to pallet, slip sheets and other unit load bases), ANSI/ITSDF B56.5-2012 (safety standards for driverless AGVs and automated functions of manned industrial vehicles), ANSI MH10.8.1-2005 (specifications regarding minimum requirements for 2 dimension symbol and linear barcode labels) and ANSI MH10.8.12-2011 (format specifications for messages and data passed between material handling trading partners).

## Slide 8: Things to Consider
When you’re preparing for an automated vehicle system purchase, you need to first consider a number of things.
1. How complex is the space your AGV must navigate? Is it simple and uncluttered enough for a fixed path system, or would you benefit more from a free-range system?
2. If you are considering a fixed path automated system, how much space do you have? Do you want an overhead system or a system using something like tape?
3. Does your AGV need to fit into tight spaces? If so, you may want a smaller vehicle.
4. How many automated vehicles do you want?
5. Does your application require just moving, or do you want something to help you assemble parts as well? This will influence the type of automated vehicle you purchase.

## Slide 9
6. What is your budget? Having a small budget doesn’t mean that you can’t get as nice an AGV as you want; it just means your supplier will approach reconstruction differently.
7. What is your timeline? Can the prospective supplier meet your deadline while maintaining quality?
8. Where do you need your AGV delivered? It is important you make sure that a manufacturer can actually deliver to you.
Once you’ve figured answered these questions, you can get down to the business of selecting your AGV manufacturer.

## Slide 10: Required Components
Components that most AGVs have in common include:
Traction motors.
traction batteries.
A computer interface and payload interface.
Traction motors assist in movement, while traction batteries provide the power. Usually, these are lithium ion phosphate batteries. The computer lets the main control processor contact the AGV and give it instructions. The payload interface is the material handling component. Examples include: conveyors, forks and loading decks.

## Slide 11: Benefits of AGVs
Increase efficiency and productivity
Consistent costs
Flexibility
Less space required
Improved safety

## Slide 12: THANK YOU